D_Δ(bold %rho,bold x,bold θ) = 0.12184k^{2}L_0^{5/3} int_0^H dzC_n^2(z) %UxE114 2I(0)-I(f_0%rho) - I(f_0%rho(1-%gamma)) + I(f_0 lline bold %rho-%gamma bold x + z bold %theta rline) newline - I(f_0 lline %gamma bold x - z bold %theta rline) - I(f_0 lline %gamma(bold %rho- bold x) - z bold %theta rline) + I(f_0 lline (1-%gamma)bold %rho + %gamma bold x - z bold %theta rline)%UxE115
ATF( bold %rho/%lambda,bold %theta ) = int d bold x P( bold x)P(bold x + bold %rho )exp( -0.5 times D_%DELTA(bold x,bold %rho,bold %theta) )
Anisoplanatism model investigations
Olivier Beltramo-Martin, Carlos M. Correia

2017-05-11

1. Purpose

We aim in this KASP note at describing the methods deployed so far to get the anisoplanatisms filter (both focal and angular) using theoretical or simulation approaches. We've compared different techniques which are all designed to provide an “OTF ratio”; the ratio between the OTF diffraction limit (OTFDL) including anisoplanatism and OTFDL :

- End-to-end simulation: using OOMAO, we propagate two sources located at a given separation through an atmosphere associated to a telescope. We then collect phase screens for both sources and derive the auto-covariance of the phase difference which feeds a routine providing the OTF.
- Zonal derivation: The auto/cross-covariance matrices are calculated from the atmosphere parameters through the point-wise integral calculation of the covariance between two sampled phase points. The auto-covariance of the anisoplanatic phase is thus coming from the sum of phase auto-covariance for both sources, minus twice the cross-correlation ([Fusco2000]) . This anisoplanatic covariance is the input of a routine taking this expression for providing the OTF.
- Flicker's method: We explore the Flicker's method ([Flicker2008]) that describes a generalized expression between the anisoplanatic phase structure function as function of the atmosphere and the geometry of the problem. Contrary to the zonal approach; actually the Flicker's one is zonal as well; we derive directly the OTF from the structure function without expressing the covariance.
- Zernike derivation: We calculate the phase auto-covariance and cross-covariance between the two sources in the Zernike domain using OOMAO routines, based on the atmosphere+telescope definitions and a given number of modes. The anisoplanatic covariance is derived as the way as it's done for the zonal approach.
- Spatial frequencies approach: the angular anisoplanatism is yielded into the Fourier domain by derivating its PSD based on works from From [Rigaut1998]. Assuming the spatial stationarity of the phase, the covariance is calculated as the Fourier transform of this PSD allowing to derive the OTF in a straightforward fashion.

2. Filters implementation
2.1 Simulated filter

The anisoplanatism covariance is evaluated in simulating the electric field propagation of two sources (any location and height), respectively src the on-axis source and gsRef the off-axis source, propagated through the atmosphere and telescope. The following scheme is repeated along 1000 temporally independent frames. Fonction draw(tel) allows to renew phase screens for each defined altitude that are following a Kolmogorov statistics with a given set of (r0,L0).
This method should provide the more accurate ATF considering two main restrictions:
- The convergence: we need to accumulate enough independent phase screens for ensuring the covariance matrix to converge. In this work 1000 frames has looked quite sufficient.
- The phase sampling: we've sampled the phase in the pupil using 81 pixels. Less on that leads to miss higher spatial frequencies to 1/2d with d=D/(#pixel-1) and introducing a fitting error.
draw(tel);
gsRef	= gsRef.*tel;
phOff	= gsRef.meanRmPhase;
src	= src.*tel;
phOn	= src.meanRmPhase;
phAni	= phOff - phOn;
Csimu	= Csimu + phAni(:)*phAni(:)' ;
otfDL	= psfrTools.zonalCovarianceToOtf(0*Csimu,npsf,D,pitch,tel.pupilLogical,src.wavelength);
ATF	= psfrTools.zonalCovarianceToOtf(Csimu,npsf,D,pitch,tel.pupilLogical,src.wavelength)./otfDL;

2.2 Zonal derivation

The anisoplanatic phase is defined as:
φΔ(r) = φ1(r) – φ2(r),
introducing the anisoplanatic covariance as:
CΔ(ρ) = <φΔ(r)φΔ*(r+ρ)> = <φ1(r)φ2*(r+ρ)> + <φ1(r)φ2*(r+ρ)> - <φ1(r)φ2*(r+ρ)> - <φ2(r)φ1*(r+ρ)>
= C11(ρ) + C22(ρ) – C12(ρ) – C21(ρ),

where the covariance matrices involved here can be produced analytically by integration of the phase resolution elements couples along altitude layers. In the case of focal anisoplanatism, C11 and C22 are different in describing the phase through respectively a cylinder and a cone.

C22	= phaseStats.spatioAngularCovarianceMatrix(npt,D,atm,gsRef,'mask',tel.pupilLogical);
[C11,C12]	= phaseStats.spatioAngularCovarianceMatrix(npt,D,atm,src,gsRef,'mask',tel.pupilLogical);
Czonal	= C11 + C22 – C12{1} - C12{1}';
otfDL	= psfrTools.zonalCovarianceToOtf(0*Czonal,npsf,D,pitch,tel.pupilLogical,src.wavelength);
ATF	= psfrTools.zonalCovarianceToOtf(Czonal,npsf,D,pitch,tel.pupilLogical,src.wavelength)./otfDL;

2.3 Flicker's method

Flicker has proposed in [Flicker2008] a generalized expression of the anisoplanatic phase structure function DΔ(ρ,x,θ) for finite altitude sources and atmospheres described by a Cn2(h) profile and an outer scale value:

2.4 Zernike derivation

nm	= 100;
zern	= zernike(2:nm,'resolution',npt,'D',D,'pupil',tel.pupil);
otfDL	= psfrTools.modes2Otf(zeros(nm-1),zern.modes,zern.pupil,npsf,1);
Czz_auto	= phaseStats.zernikeCovariance(zern,atm);
Czz_cross	= phaseStats.zernikeAngularCovariance(zern,atm,[src,gsRef]);
Czzani	= 2*Czz_auto – Czz_cross - Czz_cross';
ATF	= psfrTools.modes2Otf(Czzani,zern.modes,zern.pupil,npsf,1,'Vii')./otfDL;

2.5. Spatial frequencies approach

We've based this calculation on the spatialFrequencyAdaptiveOptics library included into OOMAO that delivers directly the anisoplanatic PSD as derived by [Rigaut1998].
n	= 101;
fao	= spatialFrequencyAdaptiveOptics(tel,atm,n,0,0,1e-3,0,2*n,'Rigaut',0,0);
ps	= 2*fao.fc/size(fao.fx,1);
fao.src	= src;
psdAniso	= fao.anisoplanatismPSD();
ATFtmp	= fftshift(abs(fourierTools.psd2otf(psdAniso,ps)));
ATFfourier	= psfrTools.interpolate(ATFtmp,npsf).*otfDL./otfDL;

4. Results

NGS aniso	0”					20”					40”
method	Sim	Zon	Fli	Zer	PSD	Sim	Zon	Fli	Zer	PSD	Sim	Zon	Fli	Zer	PSD
L0 = 100	1	1	1	1	1	0.455	0.450	0.449	0.504	0.484	0.185	0.178	0.177	0.200	0.213
L0 = 50	1	1	1	1	1	0.479	0.467	0.466	0.522	0.494	0.195	0.194	0.194	0.219	0.226
L0 = 10	1	1	1	1	1	0.634	0.627	0.626	0.695	0.636	0.442	0.433	0.432	0.478	0.446
LGS aniso	0”					20”					40”
L0 = 100	0.806	0.792	0.797	0.843	x	0.444	0.438	0.437	0.458	x	0.192	0.187	0.187	0.203	x
L0 = 50	0.818	0.808	0.812	0.859	x	0.465	0.459	0.458	0.480	x	0.210	0.205	0.205	0.222	x
L0 = 10	0.867	0.858	0.861	0.910	x	0.635	0.625	0.623	0.665	x	0.443	0.439	0.438	0.473	x

5. References
[Flicker2008]:	R. Flicker, “PSF reconstruction for Keck AO Phase 1 Final Report”, internal report.
[Fusco2000]:	T. Fusco et al, “Characterization of adaptive optics point spread function for
anisoplanatic imaging. Application to stellar field deconvolution”, A&A, 2000
[Rigaut1998]:	F. Rigaut et al., “An analytical model for Shack-Hartmann-based adaptive optics	systems”, SPIE 1998