PSF-R results
Olivier Beltramo-Martin, Carlos M. Correia

2017-05-15

1. Purpose

We deliver results of PSF reconstruction for a Keck-like AO system in both NGS (on/off GS) and LGS AO (on/off TT) derived from E2E simulations using KASP in K-band.

2. AO simulations

We've simulated a Keck-like NGSAO system in taking the guide stars on-axis then 30” off-axis (θ0 =35” in K) and LGSAO for a TT star on-axis and at 15” off-axis. The atmosphere is described in the KASP note#1.

3. PSF-R method
PSFs are reconstructed using the Véran's aproach [Veran1997] based on WFS (Shack-Hartmann sampling at Nyquist) slopes. These later are provided with an additional white noise and includes aliasing because the wave-front spatial sampling at 1/2d, with d the sub-aperture size.

OTF_%varepsilon(bold %rho/%lambda) = OTF_{slopes}(bold %rho/%lambda) times ATF(bold %rho/%lambda,C_n^2(h)) times OTF_{alias}(bold %rho/%lambda,r_0) times OTF_{fitting}(bold %rho/%lambda,r_0)

5. References
[Veran1997]: J.P. Véran, Estimation of the adaptive optics long-exposure point-spread function using control loop data in JOSAA, 1997.