CLASS	NEEDS	VALUES
ATMOSPHERE/SKY	Cn2(h) profile / L0(h) profile / Wind speed/direction profile / Transmission / sky brightness	From MASS/DIMM (where??) / From MASS/DIMM + assumptions / From MASS/DIMM / 0.896 at zenith / 21.2 mag/arcsec-1/2 at .62 microns
TELESCOPE	Diameter / Pupil image / Overall troughput / Telescope jitter	10.949 / Image with spiders / Transmission path given in KAON 716 / 20 mas rms
LGS F	Launch diameter / Location / Output power / Recovered #photons/s/m2 / Representative Na structure / Temporal variability	Center launched behind M2 / 50 W / 100 ph/cm2/s/Watt delivered to mesosphere / 90km, 10km thick., 3e9 atoms/cm2 / velocity < 30m/s
LGS WFS	#sub-apertures / #pixels/sub-ap. / Pixel scale / Layout / Valid lenslets index / Wavelength / Bandwith / Read out noise / Dark current / Sampling time / Quantum efficiency	60 / 4x4 ?? / .705 ''/pixel / .689 microns / .5 times sampling time / 2.2 e- rms at 900 fps / 265 e-/pix/s / .0011s / .92 at .70 microns (see KAON 716 doc.)
TT WFS/SOURCE	Wavelength / #pixels / Pixel Scale / Read out noise / Sampling time / Quantum efficiency / separation from center / Magnitude	H / 2x2 / 50 mas/pix / 3.2 e- rms / 2 kHz
T WFS	#sub-apertures / #pixels/sub-ap. / Pixel scale / Layout / Valid lenslets index / Wavelength / Bandwith / Read out noise / Dark current / Sampling time / Quantum efficiency	5 / 4x4 ?? / .5 times sampling time / 3.7 e- rms at 100 fps / 265 e-/pix/s / .0011s / .92 at .70 microns (see KAON doc.)
DM	Number of woofer actuators / Numberof Tweeter actuators / Woofer Peak-to-valley stroke / Tweeter Peak-to-valley stroke / Woofer Influence functions / Tweeter Influence functions / Actuators location	20 / 64 / 4 microns / 1.3 microns
RTC	Delay / Controllers types / Gains / Reconstructors / Centroiding algorithm / offsets/reference slopes	5e-4 s x 2 / integrators ? / Data ? / Data ? / Data ? / Data ?
SYSTEM	DM/WFS mis-registrations: pupil shift, magnification and rotation
Imaging Camera	Wavelength / pixel Scale	H-band